## Slide 1
LORA APRS / EXTENDED TNC2 / RXT
01
Extended LoRa APRS
Plain-text TNC2 • iGate • RXT (Remote Receiver telemetry) • station telemetry • Graywolf
For radio amateurs | Technical review: Jon Adams, N7UV | September 2026
From a packet on the air
to an understandable RF network
A project overview for radio amateurs
Notes: This overview is for radio amateurs. Jon Adams, creator of RXT, is invited to review the technical content. Graywolf messages and ACK have been tested over LoRa TNC2 TCP and serial links.

## Slide 2
LORA APRS / EXTENDED TNC2 / RXT
02
Why we started
Jon’s Arizona network makes the use case concrete.
Source: Jon Adams (N7UV), field notes supplied for this review; CA2RXU iGate discussion #287
“What goes into and comes out of the transceiver is plain text.”
Keep the on-air packet readable.
Make each reception useful to operators.
FIELD REALITY
Good antennas
Good sites
Good RF filtering
Useful diagnostics
Notes: Jon describes a high-speed 433.775 MHz LoRa APRS network, an RF-first path, busy high sites, filtering requirements and a need for applications that understand plain-text TNC2.

## Slide 3
LORA APRS / EXTENDED TNC2 / RXT
03
The whole project in one view
One RF packet, several complementary ways to use it.
Sources: LoRa APRS JSON protocol draft; CA2RXU iGate RXT documentation; Graywolf RXT guide
TRACKER
originates packet
DIGI
relays + RXT
iGATE
receives + exports
GRAYWOLF
log + map + links
→
→
→
RF path + exact identity + LoRa metadata — no forced AX.25 core
Notes: Explain the RF path first. A receiver may also be a digipeater. The iGate exports both the packet and the measurements. Graywolf presents packet, station and radio-link views.

## Slide 4
LORA APRS / EXTENDED TNC2 / RXT
04
What is a TNC2 packet?
A TNC2 packet is carried as a readable line of text.
Source: LoRa APRS JSON protocol draft §3; CA2RXU LoRa receive path
F4MLV-7>APRS,WIDE1-1:>Hello from LoRa
F4MLV-7
source
APRS
destination
WIDE1-1
path
>Hello…
information
Notes: Read the line aloud: sender, destination, optional path, then information. On this LoRa APRS network the radio payload includes a short identifying prefix before the text in TNC2 format.

## Slide 5
LORA APRS / EXTENDED TNC2 / RXT
05
The extended identity model
The identity is preserved exactly as transmitted.
Sources: LoRa APRS JSON protocol draft §3; Graywolf tnc2.PacketAddress
F4JJE-16
numeric suffix beyond 15
NN7LE-GS
letters in the suffix
NN7LE-S*
relay mark retained
Preserved on TNC2/JSON; rejected—not rewritten—at AX.25 boundaries.
Notes: The suffix is text. Show -16 and -GS as examples, not as new fixed ranges. No need to explain integer encoding to the audience.

## Slide 6
LORA APRS / EXTENDED TNC2 / RXT
06
AX.25 is a boundary—not the LoRa core
LoRa APRS is already a native digital path.
Sources: Graywolf direct LoRa TNC2 and RXT guides; LoRa APRS JSON protocol draft
01
Native LoRa core
Exact identities + RSSI/SNR/FO/TTH stay attached.
02
No forced detour
Avoid TNC2 → AX.25 → KISS → AX.25 → TNC2.
03
AX.25 at the edge
Convert only where equipment or a protocol requires it.
Notes: This is the architectural break that explains the fork. Graywolf does not remove AX.25: conventional radios, KISS links and legacy interfaces still use it. But the LoRa APRS path no longer has to convert TNC2 into AX.25, wrap it in KISS, decode it again and reconstruct TNC2. The native path preserves exact textual identities, binary information bytes and LoRa measurements such as RSSI, SNR, frequency offset and time-to-hop. AX.25 conversion happens only at a checked boundary that actually requires canonical AX.25 addressing.

## Slide 7
LORA APRS / EXTENDED TNC2 / RXT
07
The iGate at the centre
The iGate associates received packets with radio measurements and exports both.
Sources: CA2RXU iGate README and docs/RXT.md; Graywolf TNC2 release notes 546556a6
RECEIVE
LoRa packet + local RSSI/SNR/FO
RELAY
Eligible packets, with RXT on RF
EXPORT
Clean packet + structured measurements
CONNECT
Native TNC2 TCP/serial, RX + TX
Notes: This project uses the CA2RXU iGate firmware. The iGate receives LoRa packets, may relay eligible packets, sends JSON/RXT observations to Graywolf, and exchanges native TNC2 text with Graywolf over TCP or serial. The transceiver can transmit Graywolf messages on LoRa RF.

## Slide 8
LORA APRS / EXTENDED TNC2 / RXT
08
RXT follows the real RF path
Remote Receiver Telemetry was developed by Jon Adams, N7UV.
Sources: CA2RXU iGate docs/RXT.md; LoRa APRS JSON protocol draft §6
CAVECR → SOMTNX → TSRXBX
Jon’s example at SOMTNX: −71 dBm • ≥ 12 dB • +241 Hz • 594 ms.
The digi forwarded the packet to TSRXBX without Internet at the relay.
Notes: A relay appends a compact four-character tuple describing its reception and retransmission. Further capable relays can add their own tuples. The iGate strips the RF-only trailer from the clean packet and reports the measurements separately.

## Slide 9
LORA APRS / EXTENDED TNC2 / RXT
09
Four numbers, four questions
What happened at this relay?
Source: CA2RXU iGate docs/RXT.md §RF format
RSSI
Signal level
How strongly was it heard?
SNR
Signal / noise
How clear was it?
FO
Frequency offset
What frequency offset was measured?
TTH
Time to hop
How long until the relay finished?
Notes: RSSI is received level. SNR is signal relative to noise. FO is frequency offset. TTH measures end-of-reception to end-of-retransmission and includes queueing, channel access, and airtime. Do not infer congestion from one number alone.

## Slide 10
LORA APRS / EXTENDED TNC2 / RXT
10
RXT makes the route visible
A schematic of Jon’s RF-only relay example.
Schematic based on Jon Adams (N7UV) field notes; node positions are illustrative
CAVECR
originating station
SOMTNX
RF-only digipeater
TSRXBX
receiving station
→
→
RXT shows how each relay received the packet.
Notes: This is a network schematic, not a geographic map or an RF coverage prediction. It shows the packet crossing SOMTNX before being heard by TSRXBX. The relay does not need an Internet link.

## Slide 11
LORA APRS / EXTENDED TNC2 / RXT
11
Read one measured hop
The numbers come from Jon’s CAVECR → SOMTNX example.
Source: Jon Adams (N7UV), field notes supplied for this review; values are one observed packet
CAVECR → SOMTNX
RSSI
−71
dBm
SNR
≥ +12
dB
FO
+241
Hz
TTH
594
ms
One packet, one relay, four measured values.
Notes: Jon reported a CAVECR packet heard at SOMTNX with -71 dBm RSSI, at least +12 dB SNR, +241 Hz frequency offset and 594 ms time to hop. These values describe one observed reception, not a network-wide norm.

## Slide 12
LORA APRS / EXTENDED TNC2 / RXT
12
RXT and APRS telemetry
Two useful answers to different operator questions.
Sources: CA2RXU iGate docs/RXT.md §§RF format, APRS telemetry activity rates
RXT
One packet, one RF hop
RSSI • SNR • FO • TTH
“How well did the digi hear me?”
APRS TELEMETRY
Station health and activity
Battery • received • relayed • dropped
“How is the site doing?”
Notes: RXT is about one reception at one hop. APRS station telemetry is about the station itself. Avoid mixing station battery and packet RSSI on one chart without labelling their sources.

## Slide 13
LORA APRS / EXTENDED TNC2 / RXT
13
Station telemetry in practice
The iGate can show named measurements and their units.
Visual: CA2RXU iGate APRS Telemetry dashboard, field screenshot, 2026-09-23
Battery voltage and traffic rates describe the site; RXT describes radio hops.
Notes: This example shows battery voltage and RX, relay, and drop rates in packets per hour. Labels and units depend on station telemetry metadata being received. The rates are a separate APRS telemetry feature; they are not RXT values.

## Slide 14
LORA APRS / EXTENDED TNC2 / RXT
14
Why add a JSON stream?
Keep the packet and the radio context together.
Source: LoRa APRS JSON Event Protocol draft 1.0 and VALIDATION.md
1
Exact packet
including binary
Mic-E
2
Radio context
local RX + RXT hops
3
Continuity
resume after disconnect
The radio packet stays authoritative. The metadata explains its journey.
Notes: Do not show raw JSON to a nontechnical audience. Explain that the stream is a delivery envelope: original packet, local measurements, RXT measurements and a receipt number so Graywolf can resume after a disconnect.

## Slide 15
LORA APRS / EXTENDED TNC2 / RXT
15
Graywolf: the operator view
One place to inspect packets, stations, and measured links.
Sources: Graywolf RXT guide and field-validated Mic-E path, 2026-09-21
PACKET LOG
Original text
Decoded APRS when possible
STATION MAP
Position and identity
No suffix rewriting
RXT VIEW
Measured links
Recent RF history
Notes: Graywolf can consume multiple iGate JSON streams independently. It logs the clean packet, decodes applicable APRS data, shows stations on the map and recent RXT links. This reception path was field-validated with a real Mic-E beacon.

## Slide 16
LORA APRS / EXTENDED TNC2 / RXT
16
Direct TNC2, configured in Graywolf
TCP and serial reception; one explicitly authorized transmit path.
Source: Graywolf direct LoRa TNC2 guide, commits 058cc9b4–47c741e6, 2026-09-24/25
SETTINGS → TNC2
TCP + serial RX
Saved and applied immediately
EXPLICIT TX SAFETY
One transport • source • channel
TNC packet-size limit enforced
Messages + retries + beacons now share the authorized TNC2 channel.
Notes: Settings → TNC2 now saves TCP and serial connections in graywolf.db and applies them immediately. Both may receive, but only one transport, exact source identity and Graywolf channel are authorized for TX. Messages, retries and beacons on that channel use native textual TNC2. Other channels keep strict AX.25/KISS validation.

## Slide 17
LORA APRS / EXTENDED TNC2 / RXT
17
The LoRa path is bidirectional
Native TNC2 for exchanges; JSON/RXT for reception measurements.
Sources: Graywolf TNC2 release notes 546556a6; CA2RXU iGate TNC documentation
GRAYWOLF
messages + retries
LILYGO T3
iGate / TNC2 transceiver
LoRa RF
stations + digis
↔
↔
iGate → JSON/RXT reception measurements → Graywolf
AX.25/KISS stays at compatibility boundaries.
Notes: Explain the two arrows: Graywolf exchanges native TNC2 text with the LilyGO T3 iGate/transceiver over TCP or serial, and the iGate exchanges packets by LoRa RF. A separate JSON/RXT stream carries reception measurements into Graywolf. Conventional VHF AX.25/KISS is a different radio path. No AX.25 conversion is part of the LoRa TNC2 path.

## Slide 18
LORA APRS / EXTENDED TNC2 / RXT
18
What is now demonstrated?
Field evidence after the latest Graywolf RXT updates.
Sources: Graywolf TNC2 and RXT guides; field validation recorded 2026-09-24/25
RX + LINKS
Mic-E RF → iGate JSON → Graywolf packet and measured link.
TX + BEACON
Messages + ACK on TCP/serial; position beacon observed over RF.
EXTENDED ID
F4MLV-MC preserved through native TNC2, JSON/RXT and identified RF link.
Notes: Real RF Mic-E reception and link observation are field-validated. Messaging with ACK was tested over native TNC2 TCP and serial. A Graywolf position beacon sent through native TNC2 was observed by another iGate and on aprs.fi with an RXT trailer. F4MLV-MC validated extended-identity message reception and the complete JSON/RXT beacon path, including correct RF-link identification.

## Slide 19
LORA APRS / EXTENDED TNC2 / RXT
19
Jon’s Arizona network
The software must meet the needs of real radio sites and their operators.
Source: Jon Adams (N7UV), field notes supplied for this review; public CA2RXU discussion #287
433.775 MHz • BW125 • SF7 • CR4:6
Jon reports about 4.56 kbps on this regional network.
High sites and RF filtering make the coverage useful.
Notes: Jon reports the Arizona network on 433.775 MHz with BW125, SF7 and CR4:6. His coverage and pricing figures are field reports from a particular time and network, not general promises. Good filtering matters at shared high sites and in vehicles.

## Slide 20
LORA APRS / EXTENDED TNC2 / RXT
20
Where should we test next?
Questions for operators and network builders.
Technical review invited from Jon Adams, N7UV | September 2026
Which other suffix forms and applications should we validate?
Does the RXT display answer the questions operators ask?
Which sites and multi-hop radio paths should we test next?
Notes: Invite technical feedback on additional suffix forms, longer multi-hop RXT captures and broader sites. Native TNC2 messaging, beacon RF transmission and the F4MLV-MC JSON/RXT path have now been field-validated; the next step is to broaden testing across more stations, sites and RF topologies.

## Slide 21
LORA APRS / EXTENDED TNC2 / RXT
21
Sources and acknowledgements
Project documents and field evidence used in this preview.
Jon Adams (N7UV): RXT concept and field feedback • Ricardo Guzman (CA2RXU): iGate firmware
Jon N7UV field account and CA2RXU public discussion #287
github.com/richonguzman/LoRa_APRS_iGate/discussions/287
LoRa APRS JSON Event Protocol draft 1.0
github.com/moricef/LoRa_APRS_JSON_Protocol
CA2RXU iGate RXT implementation and documentation
github.com/moricef/LoRa_APRS_iGate
Graywolf extended TNC2 / RXT implementation
github.com/moricef/graywolf/tree/feature/rxt-telemetry
Notes: The links identify project repositories. The protocol is draft 1.0; the working implementations are branch-specific. Credit screenshots to their corresponding iGate and Graywolf projects.