## Slide 1
LORA APRS / TNC2 / RXT / CODE
01
Understanding the LoRa APRS project
Extended TNC2, RXT, station telemetry and Graywolf
English edition, 15 October 2026. iGate rxt code: 2cebfe6
From a radio packet
to useful information for operators
How the CA2RXU firmware has evolved
Notes: This presentation explains how the iGate fork works and how it connects to Graywolf. It covers the overall changes relative to the CA2RXU base, then the RXT and native-frame changes through commit 2cebfe6. Devices already deployed are not assumed to run that same revision. The question of the RX_rate, RelRate and DrpRate spike is deferred to a separate task.

## Slide 2
LORA APRS / TNC2 / RXT / CODE
02
The CA2RXU base and the fork
The fork builds on Ricardo Guzman’s firmware.
References: rxt Git history; src/LoRa_APRS_iGate.cpp; docs/RXT.md
The base provides LoRa radio, APRS relaying and Internet gating.
The fork adds RXT and the JSON stream.
It extends routing and message replies.
OPERATOR USE
RF links
Identities
Relaying
Evidence
Notes: The CA2RXU base already provides LoRa, APRS-IS iGate operation, digipeating, TNC interfaces and the WebUI. Those functions should not be attributed to the fork. The fork history includes work on RXT, the JSON reception stream, telemetry activity rates, regional aliases, learned return paths, local replies, authenticated remote control and native radio transport. These additions extend several existing processing paths rather than replace the whole firmware. Consult git log and the relevant modules when attributing a particular fix.

## Slide 3
LORA APRS / TNC2 / RXT / CODE
03
Roles in the network
One packet connects several distinct functions.
References: src/LoRa_APRS_iGate.cpp; docs/RXT.md; Graywolf docs/wiki/rxt-telemetry.md
TRACKER
originates packet
DIGI
relays with RXT
iGATE
receives and exports
GRAYWOLF
log and map
→
→
→
One device can combine digi, iGate and TNC interface roles
Notes: A tracker creates APRS content. A digipeater retransmits a reception after applying path rules. An iGate connects radio and APRS-IS. Graywolf stores and presents receptions, positions and measurements. One board can combine several roles depending on its configuration. RXT does not require Internet access at every relay: measurements travel over RF to the receiver that exports them.

## Slide 4
LORA APRS / TNC2 / RXT / CODE
04
The TNC2 packet
A text header describes the source, destination and path.
References: src/lora_utils.cpp; src/aprs_json_utils.cpp; Graywolf TNC2 model
F4MLV-7>APRS,WIDE1-1:>Hello LoRa
F4MLV-7
source
APRS
destination
WIDE1-1
path
>Hello…
information
Notes: In SOURCE>DEST,PATH:INFORMATION, > ends the source and the first colon ends the header. The first information byte usually identifies the APRS data type, for example > for status. The TNC2 header is textual, but the information field may contain binary bytes, especially Mic-E. A displayable line therefore does not always faithfully represent every byte. The JSON stream uses Base64 as its authoritative copy.

## Slide 5
LORA APRS / TNC2 / RXT / CODE
05
Extended identities
TNC2 and JSON retain the exact received address text.
References: src/aprs_json_utils.cpp; Graywolf docs/wiki/lora-tnc2-transceiver.md
F4JJE-16
numeric suffix above 15
NN7LE-GS
alphabetic suffix
NN7LE-S*
relay mark preserved
The iGate’s KISS encoder may alter these suffixes. TNC2 retains them.
Notes: The textual model can retain an opaque suffix after the hyphen, such as -GS, or a number above 15. Preserving a reception does not mean every protocol and function will subsequently accept that identity. Graywolf checks exact representability when it outputs AX.25. In the iGate, encodeAddressAX25 in src/kiss_utils.cpp uses toInt and does not provide that same strict validation. Avoid relying on its KISS output to preserve extended identities. APRS-IS admission and relay rules are also distinct from JSON preservation.

## Slide 6
LORA APRS / TNC2 / RXT / CODE
06
TNC2 and the AX.25 boundary
The direct text path retains extended identities.
References: src/tnc_utils.cpp; src/kiss_utils.cpp; Graywolf TNC2 guide
01
Direct TNC2
Text packets over TCP or serial, without AX.25 conversion.
02
KISS / AX.25
Compatibility with AX.25 software and equipment.
03
Specific limit
Graywolf refuses unrepresentable identities on its AX.25 output.
Notes: Direct TNC2 carries text records over a serial port or TCP connection. KISS carries binary AX.25 frames. Selecting TNC2 avoids AX.25 conversion when the radio and application already exchange text. In the iGate, tnc.kissProtocol selects the mode for serial and TCP. The TNC server port is defined as 8001 in src/tnc_utils.cpp. Graywolf refuses identities that cannot be represented exactly in AX.25 during conversion. Do not extend that guarantee to the iGate’s historical KISS encoder.

## Slide 7
LORA APRS / TNC2 / RXT / CODE
07
The packet path in the iGate code
The main loop dispatches reception to the enabled functions.
References: src/LoRa_APRS_iGate.cpp; src/lora_utils.cpp; src/station_utils.cpp
RECEIVE
Radio bytes and local measurements
RELAY
Eligible path and queued context
EXPORT
Clean packet to applications
INTERFACES
TNC2, JSON, APRS-IS and MQTT
Notes: In the LoRa_APRS_iGate.cpp main loop, receivePacket reads the radio and produces the packet and a copy for the JSON producer. Local context is captured before another radio operation can change the measurements. Accepted packets then reach the APRS-IS and digi functions when enabled. RXT hops are decoded for JSON, the Web dashboard and TNC outputs. MQTT and the SD log follow their own conditions. Non-empty CRC-valid payloads rejected by syntax or application policy can still be preserved by the JSON path in normal operation, outside ecoMode.

## Slide 8
LORA APRS / TNC2 / RXT / CODE
08
RXT describes a remote reception
Jon Adams, N7UV, developed the RXT concept.
Historical example retained from the September presentation; docs/RXT.md
CAVECR → SOMTNX → TSRXBX
SOMTNX measures its reception of CAVECR and relays the packet with RXT.
TSRXBX obtains that measurement alongside its own local reception.
Notes: In this September example, the measurements carried by SOMTNX describe its reception of CAVECR. They do not describe TSRXBX receiving SOMTNX. The latter is the final receiver’s local measurement. Combining the path, relay tuples and local measurement allows the application to describe several directed RF links. A link without measurements must not receive an invented quality value. These example names do not establish the current site inventory.

## Slide 9
LORA APRS / TNC2 / RXT / CODE
09
The four RXT measurements
Each tuple describes a relay’s reception and forwarding delay.
References: src/lora_utils.cpp; docs/RXT.md. Current SNR range: −24 to +20 dB.
RSSI
Received level
Receiver power level, in dBm
SNR
Signal / noise
Measured ratio, in dB
FO
Frequency offset
Measured offset, in Hz
TTH
Relay delay
End of reception to end of transmission
Notes: RSSI gives a signal level and SNR the signal-to-noise ratio measured by the receiver. FO is the observed frequency offset, which alone cannot assign all error to one oscillator. TTH runs from reception completion to relay transmission completion. In the code it includes queue dwell time, CAD/DIFS/backoff channel waiting and calculated airtime for the transmitted frame. It is therefore not just processor execution time. RXT values are quantized: current SNR is -24 to +20 dB in 0.5 dB steps, RSSI is -130 to -41 dBm, FO is nonlinear and TTH is exponential and scaled by the LoRa profile.

## Slide 10
LORA APRS / TNC2 / RXT / CODE
10
RXT v2: identifying the relay
A text tuple contains an identifier and four measurements.
References: src/rxt_protocol.cpp; docs/RXT.md; test/rxt_host/rxt_host_test.cpp
01
Five characters
I identifies the relay. R, S, F and H encode the measurements.
02
Name fingerprint
FNV-1a of the callsign, modulo 89. The path supplies candidate names.
03
Visible ambiguity
If several relays remain possible, no definite owner is assigned.
Notes: Text v2 adds an I character ahead of the four measurements. It fingerprints the callsign actually written into the path, uppercase, with suffix and without the star: 32-bit FNV-1a, modulo 89, plus 33. It is neither a globally unique identifier nor a central registry. The decoder compares fingerprints with used relays and their order. Order can resolve a collision when enough tuples establish it. If tuples are missing and several owners remain possible, identity_status is unresolved. A path cannot recover a callsign that no relay wrote into it. The firmware retains at most three tuples and adds no RXT to APRS messages, ACKs or REJs, including encapsulated ones.

## Slide 11
LORA APRS / TNC2 / RXT / CODE
11
The hidden RXT block in text mode
The APRS packet precedes the zero byte. Measurements follow.
References: src/rxt_protocol.cpp, toExtensionPayload / fromExtensionPayload; docs/RXT.md
TNC2 then 00 01 IRFSH
Firmware that reads a C string stops at 00 and retains the APRS packet.
A conventional relay can therefore forward the text without the RXT measurements.
Notes: Bytes 3C FF 01 identify LoRa text transport. A packet with recognized RXT is followed by 00, marker 01 and tuple characters without braces. toExtensionPayload performs the separation. fromExtensionPayload checks the extension against the path before reconstructing the internal trailer representation. C-string readers stop at zero and process only the original packet. This prevents those iGates from forwarding appended RXT in the APRS information field to APRS-IS. Compatibility depends on this reading behavior and is not guaranteed for every third-party firmware. In the internal text representation, recognizing a comment that resembles a trailer still carries a collision risk. Native RXT remains separate.

## Slide 12
LORA APRS / TNC2 / RXT / CODE
12
The native radio frame
Compact binary transport that reproduces the exact TNC2 packet.
References: src/native_aprs.cpp; src/lora_utils.cpp; native frame draft 0
01
RF prefix
3C FF 02 for native frames, rather than 3C FF 01 for text.
02
Compact coding
Compact addresses and positions. Huffman text when shorter.
03
TX selection
0 text by default, 1 native, 2 text then native for trials.
Notes: Native frame draft 0 carries the same TNC2 content compactly. Common addresses use short coding, unusual forms can remain textual, supported positions use binary coding, and remaining text can use Huffman coding when shorter. The encoder decodes its own result to verify exact reconstruction. A layout that cannot be reproduced by specialized coding uses the raw information field. If the complete frame cannot be encoded, transmission falls back to text. Messages and Mic-E can therefore travel in a native envelope with raw information, without specialized semantic compression. Mode 2 sends two copies for coexistence trials. This experimental format does not itself increase transmit power or receiver sensitivity.

## Slide 13
LORA APRS / TNC2 / RXT / CODE
13
Preserving native RXT identity
Since the 13 October fix, native RXT remains separate from the text.
References: src/native_aprs.cpp, remapRxt; src/station_utils.cpp; RF validation on 13/10
RECEPTION
Each measurement identifies a precise position in the path.
QUEUED
The packet retains its measurements despite a later reception.
RELAY
Indexes follow full callsigns after the path changes.
Notes: Native RXT contains a path-position mask and four measurement bytes per selected position. It does not need the text fingerprint to identify an owner. Since fix 2cebfe6, the TNC2 packet and indexed context remain separate during reception and queueing. remapRxt follows full callsigns when path rewriting removes an alias. A removed path entry loses its measurement. Repeated callsigns can be associated by occurrence only when their occurrence count is unchanged. The v2 tuples derived for logs do not replace native context. A later text output nevertheless returns to fingerprint-based attribution. The 13 October trials use F4MLV-18 and F6DEV-10, both fingerprint C, with only one measurement, then check RF retransmission and queued delay.

## Slide 14
LORA APRS / TNC2 / RXT / CODE
14
The path and its measurements
The path identifies used relays. RXT supplies their measurements.
Jon’s historical example; illustrative positions. Reference: docs/RXT.md
CAVECR
originating station
SOMTNX
RF-only relay
TSRXBX
receiving station
→
→
Relay without RXT: known path, no RF measurements
Notes: A used callsign in the path identifies the declared passage through that relay, but does not automatically supply measurements. The decoder reports hops without data as NA. The used portion ends at the last path entry marked *. The code accepts both multiple-star paths and the convention in which only the last used relay carries a star. Entries after that last * are not presented as completed hops.

## Slide 15
LORA APRS / TNC2 / RXT / CODE
15
Reading a historical measurement
Jon’s example of SOMTNX receiving CAVECR.
Source: September presentation, Jon’s example. Historical SNR value, before the range extension.
CAVECR → SOMTNX
RSSI
−71
dBm
SNR
≥ +12
dB
FO
+241
Hz
TTH
594
ms
SNR was capped at the time. The current range reaches +20 dB.
Notes: These values come from Jon’s example in the original PowerPoint. They are not new measurements made for this update. The ≥ sign before +12 dB reflects the encoding range at the time. The current code extends SNR to +20 dB, and the same character must not be interpreted using the old scale. The 594 ms TTH is that relay’s delay for that packet, not a network average.

## Slide 16
LORA APRS / TNC2 / RXT / CODE
16
RXT and station telemetry
RXT describes a hop. Telemetry describes the station.
References: src/telemetry_utils.cpp; docs/RXT.md
RXT
One packet and one RF hop
RSSI, SNR, FO and TTH
How did the relay hear this packet?
APRS TELEMETRY
Station health and activity
Voltages and rates in packets/hour
How active is the site?
Notes: RXT carries measurements attached to one specific reception. Station telemetry aggregates voltages and activity counters. In telemetry_utils.cpp the rates use the counters and actual elapsed time, in packets per hour. RX_rate counts accepted receptions after blacklist filtering, RelRate counts packets accepted into the digi queue, and DrpRate counts application-rule rejections. These sets are not a delivery balance: RX_rate = RelRate + DrpRate is not a code invariant. The rate spike reported by Jon is not analyzed here.

## Slide 17
LORA APRS / TNC2 / RXT / CODE
17
Telemetry in the WebUI
Names and units make station reports readable.
Historical screenshot, 23 September 2026; src/telemetry_utils.cpp; docs/RXT.md
Rates describe activity. RelRate counts packets accepted into the relay queue.
Notes: The September screenshot illustrates channel names and units. By itself it does not establish current firmware behavior. Activity channels are published as RX_rate, RelRate and DrpRate with pkt/h units. The code resets counters when generating a report and caps each rate at 8280. These rates currently accompany encoded voltage telemetry when at least one voltage channel is selected and weather telemetry is inactive. Relay rate counts acceptance into the queue, not confirmed radio transmission or recipient delivery.

## Slide 18
LORA APRS / TNC2 / RXT / CODE
18
The JSON reception stream
Each event associates packet bytes with their radio context.
References: src/aprs_json_utils.cpp; src/aprs_json_text.cpp; README.md
1
Exact bytes
Base64, including
Mic-E data
2
RF context
Local reception and RXT hops
3
Reconnect
Bounded replay using a cursor
Ten events in memory. A gap event reports when replay cannot satisfy the cursor.
Notes: The endpoints are /api/v1/aprs/stream for NDJSON streaming and /api/v1/aprs/events for recent events. rx records contain packet.raw_tnc2_base64 and information.raw_base64. Text projections are included only when valid UTF-8 without control characters. Local measurements, radio parameters and RXT hops are separate from the packet. The cursor combines a boot identifier and sequence. The RAM queue retains ten events. The protocol reports gap when the requested cursor can no longer be satisfied, for example after a restart or loss of retained history. This is bounded replay, not unlimited archival storage.

## Slide 19
LORA APRS / TNC2 / RXT / CODE
19
What Graywolf uses
The JSON stream feeds the packet log and measured links.
Reference: Graywolf docs/wiki/rxt-telemetry.md, local graywolf-rxt checkout
PACKET LOG
Preserved bytes
APRS decoding when possible
MAP
Known positions
Preserved identities
RXT LINKS
Measurements per link
Recent history
Notes: According to the local Graywolf guide and implementation, each JSON/RXT source is consumed independently. Graywolf preserves bytes, then derives a TNC2 packet when the envelope can be parsed. It decodes recognized APRS information and also retains receptions it cannot interpret. Remote RXT links come from the declared measurements. The final local link runs from the last used relay, or the source for direct reception, to the receiver. No local TTH is invented. Map drawing requires known positions. Green and orange express observation age, not RF quality.

## Slide 20
LORA APRS / TNC2 / RXT / CODE
20
Direct TNC2 in Graywolf
Reception and transmit permission are configured separately.
Reference: Graywolf docs/wiki/lora-tnc2-transceiver.md; src/tnc_utils.cpp
TNC2 RECEPTION
TCP and serial
Persistent settings
AUTHORIZED TX
One transport, source and channel
TNC packet-size limit
Messages, retries and beacons use the authorized TNC2 channel
Notes: Graywolf’s TNC2 page configures TCP and serial connections and persists the settings. A receive connection does not authorize transmission. TX requires a transport, an exact source identity, an authorized channel and a byte limit. Queue acceptance does not prove RF transmission or delivery. The iGate must also enable LoRa TX and use TNC2 mode. It calls trim() on incoming text: Graywolf’s guarantee about bytes written to the port does not prove that leading or trailing whitespace survives the firmware.

## Slide 21
LORA APRS / TNC2 / RXT / CODE
21
Exchanges in both directions
Exchanges over TNC2. Reception measurements over JSON.
References: src/tnc_utils.cpp; src/aprs_json_utils.cpp; Graywolf TNC2 guide
GRAYWOLF
messages and retries
TNC2 RADIO
iGate radio interface
LoRa RF
stations and relays
↔
↔
Reception measurements: iGate to Graywolf over JSON
Text TNC2 and native radio frames are distinct
Notes: Two processing paths cooperate. Messages, retries and beacons can leave Graywolf over TNC2 to a radio. Receptions and measurements arrive over JSON/RXT. JSON ingress alone does not authorize transmission. The word native can be ambiguous: direct TNC2 is a textual interface between software and a TNC, whereas the native LoRa frame is a binary radio format. Neither requires the other. The firmware can accept TNC2 and transmit text or native frames depending on lora.txFormat.

## Slide 22
LORA APRS / TNC2 / RXT / CODE
22
The message return path
The iGate learns over RF how to reach a station.
References: src/station_utils.cpp; src/aprs_return_route.cpp; docs/REVERSE_MESSAGE_ROUTING.md
01
Learned route
Used relays A then B produce return path B then A.
02
APRS-IS to RF
A message to a recently heard station uses this learned path.
03
Limited lifetime
Expired or unknown route: no APRS-IS downlink to RF.
Notes: Learning uses an actual LoRa reception, before local replies. The used path is reversed after excluding aliases and Internet elements. SOURCE>A,B*,WIDE2-1 teaches return path B,A. The first copy retained in the local window supplies the route. This favors the first arrival, not necessarily the strongest signal. A route expires with rememberStationTime and disappears on restart. Without a valid route, APRS-IS downlink messages are not transmitted and do not fall back to beacon.path. Distinguish this from local RF replies to queries, which may have a beacon.path fallback.

## Slide 23
LORA APRS / TNC2 / RXT / CODE
23
Relay and reply handling
Relaying and local processing handle their duplicates separately.
References: packet_dedup.cpp; local_message_gate.cpp; digi_utils.cpp; RF validation on 28/09
DUPLICATES
Local 25 s window for relaying and route learning.
REPLIES
Another ACK is possible without executing the same local query twice.
RF PATHS
Bounded regional aliases and a guard against returning through this relay.
Notes: Local packet_dedup uses a default 25-second window, with separate claims for relaying and route learning. Its key includes the APRS destination for Mic-E, where the destination carries position data. It does not replace APRS-IS deduplication or coordinate iGates. Local processing can send another ACK for a repeated copy to recover from a lost ACK, while avoiding another response or execution. The September fixes preserve reply-ack and make the addressed identity send the reply. Regional aliases are configurable and bounded, and the code guards against returning through its own relay. Size limits are checked before transmission: no room for RXT means relaying without a new tuple, while an oversized APRS packet is refused without truncation.

## Slide 24
LORA APRS / TNC2 / RXT / CODE
24
Authenticated radio commands
Remote control uses an authorized identity and a configured secret.
References: src/remote_auth.cpp; include/remote_replay_window.h; REMOTE_CONTROL_AUTH documentation
01
HMAC tag
The check binds the command to its sender and target.
02
Counter check
Persistent state prevents re-execution of previously received commands.
03
Specific use
This authentication applies to remote control, not every packet.
Notes: Remote control is distinct from ordinary APRS traffic and APRS-IS connection authentication. remote_auth checks the configured controller identity and an HMAC-SHA256 tag over data binding the controller, target, counter and command. A persisted counter window rejects commands already consumed. The mechanism requires a configured secret. The tag does not encrypt the command and does not authenticate every received packet. The 28 September RF validation documents acceptance of EM=OFF and rejection of its relayed duplicate without a second execution.

## Slide 25
LORA APRS / TNC2 / RXT / CODE
25
Documented tests
Each observation is limited to the setup actually tested.
References: RF tests on 28/09, 29/09 and 13/10; Graywolf RXT and TNC2 guides
RECEPTION
Mic-E and F4MLV-MC observed from radio to Graywolf.
MESSAGES
Delivery to a terminal through two physical relays, with a return ACK.
NATIVE RXT
Identity retained after path rewriting and queued delay.
Notes: The Graywolf guides describe September observations of Mic-E and extended identities. The additional 28 September validation describes delivery to a T-Deck through two physical relays isolated by radio profiles, followed by an ACK received directly by the iGate. Route learning used a synthetic packet, which limits the conclusion. The 13 October trials captured retransmitted RF bytes and validated native RXT identity with colliding fingerprints, including a queued packet. These results establish neither site coverage nor every possible radio profile and path. See the specific reports referenced on the slide.

## Slide 26
LORA APRS / TNC2 / RXT / CODE
26
Jon’s radio context
Packet durations depend on each network’s LoRa profile.
Source: September presentation and Jon’s reported observations. Not a deployment inventory.
433.775 MHz / BW125 / SF7 / CR4:6
Regional profile reported by Jon in the September presentation.
Local tests on a different profile do not measure this network.
Notes: The profile comes from Jon’s account retained in the September PowerPoint. It supplies context for the example, not the current configuration of each device. Airtime and TTH encoding depend on LoRa settings. Comparing SF7 and SF12 durations without accounting for the profile cannot isolate a code effect. Published corpus compression gains are calculations for those corpora and profiles, not measurements of capacity or coverage on Jon’s network.

## Slide 27
LORA APRS / TNC2 / RXT / CODE
27
Limits to keep in mind
Compatibility and test scope set the limits of the conclusions.
References: docs/RXT.md; docs/LORA_APRS_NATIVE_FRAME_DRAFT0.md; RF test reports
Native frames require compatible receivers.
A text relay can lose the earlier RXT measurements.
Return routing does not coordinate multiple iGates.
Notes: Native reception requires the matching codec. Firmware without support may ignore the frames, and some older fork builds handled them imperfectly as text. Text mode with a hidden extension preserves the APRS packet for readers that stop at zero, but their relays lose the hidden measurements. Text v2 fingerprints can remain ambiguous. A residual v1 trailer is not automatically translated into v2. Learned return routing supplies a route for one iGate, but does not coordinate multiple iGates independently transmitting the same downlink. These limits explain why an implemented option and a successful test do not guarantee every deployment.

## Slide 28
LORA APRS / TNC2 / RXT / CODE
28
Where to read the mechanisms
The main loop shows how packets move between modules.
Reading reference: rxt branch, commit 2cebfe6. Each slide’s notes explain the mechanisms.
LoRa_APRS_iGate.cpp: reception dispatch
lora_utils.cpp: radio, RXT context and transmission
rxt_protocol.cpp: text block, fingerprints and attribution
native_aprs.cpp: codec and RXT-to-path association
digi_utils.cpp: relay decision and path rewriting
station_utils.cpp: transmit queue and learned route
aprs_json_utils.cpp / tnc_utils.cpp: interfaces
aprs_is_utils.cpp / remote_auth.cpp: messages and control
Notes: Start in the LoRa_APRS_iGate.cpp main loop to follow call order instead of reading modules in isolation. For reception, follow receivePacket, captureRxtRxContext, the APRS-IS and digi consumers, getDecodedRxtMetrics, then recordRx and TNC outputs. For relaying, follow generateDigipeatedPacket, addToOutputPacketBuffer, processOutputPacketBuffer and sendNewPacket. rxt_protocol.cpp handles text transport and fingerprint attribution. native_aprs.cpp handles the codec and indexed association. Then consult host tests and RF reports to distinguish function guarantees from hardware observations.

## Slide 29
LORA APRS / TNC2 / RXT / CODE
29
References and contributions
The iGate scope for this edition is the code at 2cebfe6.
Ricardo Guzman CA2RXU: base firmware. Jon Adams N7UV: RXT concept and field feedback.
iGate code: rxt branch, commit 2cebfe6, 13 October 2026
docs/RXT.md and docs/RXT_V2.md
docs/LORA_APRS_NATIVE_FRAME_DRAFT0.md
docs/VALIDATION_RXT_NATIVE_RF_20261013.md
docs/REVERSE_MESSAGE_ROUTING.md
docs/RF_FIX_VALIDATION_20260928_en.md
Graywolf: docs/wiki/rxt-telemetry.md
Graywolf: docs/wiki/lora-tnc2-transceiver.md
Notes: The repository files cited on the slides are reading references. Test reports describe observations whose setups and limits must be respected. Earlier NOTE_TECHNIQUE_RXT and REPONSE_JON drafts are not used as independent evidence. The associated Graywolf checkout was read to explain its own guarantees separately from the iGate firmware’s guarantees. This document is not accompanied by publication or deployment.